## Slide 1: Bit-Slicing in Cadence
Evan Vaughan

## Slide 2: What I’m Trying to Do
No native support for bit-slicing in Cadence Synthesis Tools
  Synopsys does provide this
Trick RTL Compiler and Soc Encounter into laying out and Adder in a bit slice
Use 4 bit Kogge-Stone adder as test design

## Slide 3: Initial Synthesis
Reduce Nangate library to only necessary components
  and, or, inv, xor, aoi21
Very disordered layout

## Slide 4: Initial Synthesis Placement

## Slide 5: Second Attempt
Made no modifications to Nangate library
Want Generate/Propagate blocks to be in order on, on top row

## Slide 6: Third Try
Synthesized netlist created 4 different instantiations of a half-adder (GPGenerator) and placed them separately
I edited synthesized netlist to have one large instantiation that would be called once.

## Slide 8
no change.

## Slide 9: Fourth (current) Method
Create a new library using modified Nangate components
  Combine four half-adder blocks into one large standard cell
  Determine what other components can be combined later
Requires layout and schematic views

## Slide 10: Problems encountered
Viewing layouts
  Couldn’t directly open .oa layouts in virtuoso
  Got around this by “streaming” GDSII layout versions
Schematics
  PNG and .edif views
    Based schematic off PNG, failed LVS
    Couldn’t import .edif
    Read through .edif and found that Nangate uses low threshold models
      Still failed LVS (no power or ground connections)

## Slide 11: Continued….
Because just four blocks combined, can just edit .lib and .lef files by hand to create new cells
Shouldn’t be great performance difference between single block and four combined blocks

## Slide 12: Questions/Suggestions